## Slide 1: Design for Testability for SoC and IP’s
SoC vs ASIC/ASSP
  Has both digital and analog blocks (mixed signal functions)
  Contains many IP blocks from different suppliers
  Contains scattered memory blocks of all sizes
  Usually with more power gating and power island/domain partitions
  Hierarchical mixture of processor, custom logic,, hard macro and soft core IP, peripherals, etc
Current Practices
  Test access mechanism/wrapper design (JTAG, P1500) in SoC’s hierarchy
  Leverage computation power from big server farms to generate better ATPG
    Pattern compression by EDA tools, Sophisticated pattern and fault-grading analysis
  Broadcasting, parallel testing, re-use or re-generate patterns on chip
  IP sign-off requirements:
    Virtual Component Exchange (VCX): synthesis, DFT, ATPG validated at target node.
  Spare gates and floor-sweeping.
Chingwen Chang / Oct. 16 2016

## Slide 2: SoC DFT Challenges
Challenges from TAM wrappers:
  Impose restriction, overhead, timing delay, more levels of test access time
  Block boundary optimization, scan chain re-ordering/inversion
  More design and verification manpower.
  More complexity added to low-power designs.
  More difficult to debug and access failures.
Challenges from IP’s supplied test structure and vectors:
  Bugs in pre-supplied vectors
  Surrounding access mechanism
  Timing of the logic in test mode
  Effort in expanding the vectors to the chip level
  Debugging efforts is fraught because of IP’s different suppliers and different DFT structures
  Low-power functions can only be verified at chip level.
Solutions: MBIST + LBIST + smart ATPG
Chingwen Chang / Oct. 16 2016

## Slide 3: Background - Anna Chang
Design and Verification:
  SystemVerilog / UVM / OVM / OOP : 7 years
    Microprocessor (Sun, AMD), DFT (Apple, Nvidia, TSMC, AMD),
    JTAG (Apple, Nvidia, TSMC, AMD), MBIST (TSMC, Nvidia, Apple, AMD),
    PCI-express (Sun), mixed Signal Audio codec (Nuvoton),
    I2C, SPI, Ethernet, I2S, PCI/PCI-e, SLIMbus, AMBA, AXI, AHB, P1500 (in different projects)
  Verilog / ASIC : 15 years
    Microprocessor (Sun), and including UVM/OVM experience above.
    Synthesis, timing analysis, micro-architecture (Sun, TSMC, Nuvoton)
    FPGA Xilinx-Cortex M0 (Nuvoton and consulting projects, 18 months)
  Formal Verification (Apple, 2 years)
  Tools : VCS, NCverilog, Modelsim, Jasper, Design/DFT-Compiler, TMAX, Perforce, SVN, Git, Eclipse
DFT : 12 years in JTAG, P1500, Scan-chain, MBIST, ATPG
Design/Project Management : TSMC 4 years.
Programming Languages : Perl, Python, Make, Tcl/tk, Java, C/C++, J2EE(Spring, Hibernate, JDBC), HTML, CSS, JavaScript (Selenium, AJAX, JQuery, Node.js), XML/JSON, Linux/Unix (bash/csh/tcsh), Apache, SQL/MySQL, PHP
https://github.com/chang-anna/presentation/tree/master/public
Chingwen Chang / Oct. 16 2016